mo@MoPC-Arch

# PD2 writeup
## constants
i made the constants such that the ALU has its own set of codes that corresponds with the funct3 and funct7. all the opcodes have labeled funct3s and the different types of each opcodes are made seperate such as the different subtypes of I type.
## igen
the igen is completly combonational and always gives and output unless the opcode is R type. the immediate is muxed with the opcode.
## decode
decode is made to load on the negedge of clock. it is also completely blocking as there is no "shift register" style logic required by the design.
## control
the control is simply a mux for the different opcodes and the pcsel is changed from PCADD4 to PCIMM in branch and jump and the branch opcode needs the condition from the further instruction to be true to then change from the default PCADD4.